## Slide 1: AUTOSAR ComStack & SIO Overview

## Slide 2: Agenda
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
2
AUTOSAR Architecture
AUTOSAR Communication Stack
  CAN Driver
  CAN Interface
  CAN Transport Protocol
  PDU Router
  COM
SIO Overview

## Slide 3: Overview
AUTOSAR Architecture
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
3
Microcontroller
Microcontrollers Drivers
Memory Drivers
Communication Drivers
Service Layer
Onboard Device Abstraction
AUTOSAR Runtime Environment (RTE)
I/O Drivers
Complex
Drivers
Memory Hardware Abstraction
Communication HW Abstraction
I/O Hardware Abstraction
Application Layer
Microcontroller
Memory Services
Communication
Services
Contains internal driver – software module with direct access to uC
Interfaces for lower layer to upper layer. Also contains external driver
Provides services for application & BSW modules relating to communication.

## Slide 4: Communication Stack
Communication Bus
ECU 1
ECU 2
ECU n
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
4
Provides standardized access to the vehicle network system.
Software components can communicate with each other even if they are located on different ECUs

## Slide 5: Communication Stack
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
5

## Slide 6: Communication Stack
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
6
SDU - Service Data Unit: the data passed by an upper layer, with the request to transmit the data as well the data which is extracted after reception by the lower layer and passed to the upper layer.
PCI - Protocol Control Information: needed to pass a SDU from one instance of a specific protocol layer to another instance. Added by a protocol layer on the transmission side and is removed again on the receiving side.
PDU - Protocol Data Unit: contains SDU and PCI. On the transmission side the PDU is passed from the upper layer to the lower layer, which interprets this PDU as its SDU.

## Slide 7: CAN Driver
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
7

## Slide 8: CAN Driver - Definitions
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
8
CAN Controller: serves exactly one physical channel.
CAN Hardware Unit: may consists of one or multiple CAN controllers and CAN RAM (Mailbox) areas.
CAN Hardware Object: a PDU buffer inside CAN RAM of CAN Hardware Unit/CAN Controller.
CAN Controller
Mailbox
CAN HW Obj
CAN HW Obj
CAN HW Obj
CAN Transceiver
CAN Network

## Slide 9: CAN Driver
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
9
Performs the hardware access and offers a hardware independent API to the upper layer
Only access CanIf from upper layer.
Provide service for initiating transmission.
Calls the callback functions of the CanIf module for notifying events, independently from the hardware
Provides services to control the behavior and state of the CAN controllers.

## Slide 10: CAN Interface
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
10

## Slide 11: CAN Interface - Definitions
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
11
HOH – Hardware Object Handle: represent an abstract reference to a CAN mailbox structure (contains CanId, DLC, Data). Be instantiated into HRH & HTH. Defined and provided by the CAN Driver.
HRH – Hardware Receive Handle: is a handle referencing a logical hardware transmit object of the CAN controller mailbox.
HTH – Hardware Transmit Handle: is a handle referencing a logical hardware receive object of the CAN controller mailbox.

## Slide 12: CAN Interface - Definitions
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
12
CanIf Rx L-PDU: L-PDU handle of which the direction is set to “lower to upper layer”.
CanIfRxBuffer: single element RAM buffer located in the CAN Interface module to store whole receive L-PDUs.
CanIf Tx L-PDU: L-PDU handle of which the direction is set to “upper to lower layer”.
CanIfTxBuffer: single element RAM buffer located in the CAN Interface module to store whole transmit L-PDUs.

## Slide 13: CAN Interface
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
13
Consists of all CAN hardware independent tasks belongs to the CAN communication device drivers of the corresponding ECU.
The application data buffers are located in the upper layer. The buffer location is passed by the CAN Interface from or to the CAN Driver during transmission and reception
Events detected and processed by the CAN Driver are forwarded to the CAN Interface.
DLC check for receive PDU.

## Slide 14: CAN Interface
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
14
Transmit data flow
Receive data flow

## Slide 15: CAN Transport Protocol
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
15

## Slide 16: CAN Transport Protocol
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
16
Segment and reassemble CAN I-PDUs longer than 8 bytes for transferring diagnostic messages in a single CAN frame or in multiple CAN frames.
Event triggered so that CanTp can processes transfer of N-SDU (respectively L-SDU) coming from the PDU Router (respectively CAN Interface) directly.

## Slide 17: PDU Router
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
17

## Slide 18: PDU Router
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
18
Provides services for routing of I-PDUs:
  Communication interface modules (e.g. LINIF, CANIF, and FlexRayIf)
  Transport Protocol modules (e.g. CAN TP, FlexRay TP)
  Diagnostic Communication Manager (DCM) and Transport Protocol modules
  COM and Communication interface modules or I-PDU Multiplexer
  I-PDU Multiplexer and communication interface modules

## Slide 19: PDU Router
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
19
PDU Router routing tables: static routing tables describing the routing attributes for each PDU to be routed.
PDU Router Engine: actual code performing routing actions according to the PDU Router routing tables
Two ways of PDU transferring:
  PDU Reception
  PDU Transmission
Source path: CANIF  PDUR
Destination path: PDUR  COM
Source path: COM  PDUR
Destination path: PDUR  CANIF

## Slide 20: COM
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
20
RTE

## Slide 21: COM - Definitions
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
21
Signal: a unit of PDU which has 1 or more bit length. So called ‘Message’ in OSEK-COM.
Signal group: group of signals, be treated as an atomic unit.
I-PDU: PDU in interaction layer, consist of signals.
I-PDU group: an arbitrary collection of I-PDUs in the AUTOSAR COM module.
I-PDU
Payload
Signal
Signal group
.
.
.
I-PDU Group

## Slide 22: COM
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
22
Features:
  Provision of signal oriented data interface from RTE and packing of signals to I-PDUs to be transmitted.
  Unpacking of received I-PDUs and provision of received signals to RTE.
  Routing of signals/signal groups from received I-PDUs into I-PDUs to become transmitted.
  Communication transmission control (start/ stop of I-PDU groups).
  Monitoring of receive signals (signals timeout) (*)
For CAN and LIN the maximum PDU length is 8 bytes.
Support endianess conversion.
RTE

## Slide 23: COM
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
23
Transmission interaction model

## Slide 24: COM
AUTOSAR ComStack
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
24
Reception interaction model

## Slide 25: AUTOSAR Architecture
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
25
Microcontroller
Microcontrollers Drivers
Memory Drivers
Communication Drivers
Service Layer
Onboard Device Abstraction
AUTOSAR Runtime Environment (RTE)
I/O Drivers
Complex
Drivers
Memory Hardware Abstraction
Communication HW Abstraction
I/O Hardware Abstraction
Application Layer
VDB Runtime Environment (RTE)
Software Components – ACF, ACO, FUS….
Microcontroller
OS
FSI Software Components – NET, DIA, DAL….
MRR – VDB Architecture
Memory Services
Communication
Services

## Slide 26
SIO Overview
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
26
Application
C-Controller
C- Driver
<C IF >
Data link layer
L-PDU
<C> TP
<C> SM
Network Layer
N-PDU
NM
ComM
DCM
XCP
CSPL
dec
Pdu mon
COM
PDUR
I-PDUM
Interaction
Layer
I-PDU
pgc
Application
Layer
SMI
SMO
hrz
avi
CSP
Netlib
Diagnostics
Monitoring
CAN/FLEXRAY
ISOTP15765 -2
SIO

## Slide 27: Flow of Rx Message
SIO Overview
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
27

## Slide 28: Flow of Tx Message
SIO Overview
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
28

## Slide 29: Working flow for adding new messages
SIO Overview
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
29
1. Requirement gathering
2. Update product requirement
3. CUBEC configuration
4. Coding

## Slide 30: Conversion
SIO Overview
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
30
Raw value to physical value
Physical value = Raw value * Bus factor + Offset
?
Ego velocity: min = -50km/h; max = 150km/h
Can signal: 10 bits
 Appropriate Bus factor, Offset ?

## Slide 31: Conversion
SIO Overview
Pham Vo Hoai Anh (RBVH/ESS1) | 4/29/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
31
Physical value to VDB value
VDB value = (Physical value * Norm) / Conversion Factor
?
Ego velocity: min = -50km/h; max = 150km/h
VDB type: SWORD,
Conversion factor: 0.625 (miles/h)
 Appropriate Norm ?
VDB value = (Physical value * Norm) * Conversion Factor
For RX message:
For TX message: