## Slide 1: DGS Coding guideline Compiler Independency

## Slide 2: Table of Contents
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
2
Overview
C99 Compliance
Controller data width
Single Bit Handling
Assembler programming
Intrinsic functions

## Slide 3: Overview
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
3
In the future, DGS source code will be:
Used on several μC platforms and compiled via several compilers
Integrated in UBK and foreign ECUs

## Slide 4: C99 Compliance
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
4
Conform to ISO/IEC 9899:1999 (ISO C99) “Programming languages − C”
Some deviations and extensions are permitted for automotive applications

## Slide 5: C99 Compliance
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
5
In accordance to the recommendations given by the MISRA−C: 2004 and MISRA−C:2012
Width of C−data types
  char is 8 bit
  short is 16 bit
  int is 16 bit or 32 bit
  long is 32 bit
  If available long long is 64 bit ( for 32-bit machines)
  See Chapter 5.3 "Data types" p. 28

## Slide 6: C99 Compliance
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
6
In accordance to the recommendations given by the MISRA−C: 2004 and MISRA−C:2012
C−language implementation
  Unsigned char (resp. uint8 ) is the smallest addressable memory unit
  Unsigned char (resp. uint8 ) has the smallest alignment
  Negative numbers are represented by the two's complement
  Arithmetic shift on signed operands
  For integers, "/" operator is the algebraic quotient with any fractional part discarded
  => the expression (a/b)*b + a%b shall equal a

## Slide 7: C99 Compliance
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
7
In accordance to the recommendations given by the MISRA−C: 2004 and MISRA−C:2012
C99 limits
Nesting of parentheses | 63
Nesting of struct or union types | 63
Number of block scope identifiers in a block | 511
Number of members in struct or union | 1023
Number of enumeration constants | 1023
Nesting of control structures (statements) | 127
Number of case labels | f1023
Nesting levels of #include "%s" | f15
Nesting level of #if... | f63
Characters for Identifier | 120
Number of macro definitions simultaneously defined | 4095
AUTOSAR ememory meapping concepts or DGS tool chain related | …

## Slide 8: C99 Compliance
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
8
In accordance to the recommendations given by the MISRA−C: 2004 and MISRA−C:2012
C99 language extensions
  If the long long data type is available then the LL suffix for 64 bit constant definition is used.int is 16 bit or 32 bit
  Inline (encapsulated in a central macro definition) )
  "//" C++ style comments
  Special character: line ends are defined as CR/LF (DOS/Windows style), "$" (0x24) and "@" (0x40)

## Slide 9: Controller data width
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
9
What is controller data width?
  The controller data width reflects the maximum amount of data that processor can process and deliver at one time
  Example: a 8 bit micro controller operates on 8 bits respectively at a time
  Data overflow is an issue that should be consider. Check the following example:

## Slide 10: Controller data width
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
10
  The expected result is c = 200. But it won't be. Why?
  a + b is computed first giving 400 which is greater than 255 (8-bit limit). Hence the result will be an overflow and c will have incorrect data.
  Solution : c = a / 2 + b / 2;
  Or : c = (a >> 1) + (b >> 1);

## Slide 11: Controller data width
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
11
  DGS have only 32bit controllers in use but theoretically it is possible to integrate AUTOSAR software modules also for 16bit or 8bit controller platforms
  Upward portability must be possible (8bit −> 16bit −> 32bit)
  Downward portability (32bit −> 16bit) is not requested

## Slide 12: Single Bit Handling
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
12
  What is single bit?
  Single bit is the smallest unit of data in a computer
  A bit has a single binary value, either 0 or 1
  In most computer systems, there are eight bits in a byte
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
byte
bit
bit

## Slide 13: Single Bit Handling
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
13
  The data type _bit is not portable and shall therefore not used in the C−code.
  The only possible way to use single bits in MEDC17:
  The base types bool, boolean and bit shall be considered of BIT category
  Only Manual Code and ASCET (not Mathlab/Simulink): Variables and messages of BIT category should be specified in PaVaSt by using DAMOS−models (TYP_MsgBitNoReIni, TYP_SingleBit*).

## Slide 14: Single Bit Handling
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
14
The CATEGORY VALUE shall not be used together with bit, bool and boolean type.

## Slide 15: Single Bit Handling
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
15
In C−Code the variables and messages of BIT category and bit type shall be accessed only via the tool chain generated macros GET_, SET_, PUT_, CLR_ .

## Slide 16: Assembler programming
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
16
EXAMPLE
    #define Cpu_ResumeInt()
    /* enable interrupt system only, if it was enabled prior to calling Cpu_SuspendInt() */
    asm volatile ("jz.t %0,8,0f; enable; 0:"::"d" (stPreviousStateOfCpuIntSystem_u32):"memory");
    /* IGNORE RULE 3411: To balance Cpu_SuspendInt and Cpu_ResumeInt unbalanced brackets are used */
    } do { } while(0) /* this ugly statement is necessary to cheat MISRA checker */
    #else

## Slide 17: Assembler programming
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
17
Pros
  Software will be executed faster
Cons
  Depend on each μC and each compiler.
  Only useful in special cases like service library, complex drivers.
  The portability will be lost.

## Slide 18: Intrinsic functions
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
18
An intrinsic function (or builtin function) is a function (subroutine) available for use in a given programming language which implementation is handled specially by the compiler.
Intrinsic instructions are not portable between different compilers and μC platforms.
Do not use intrinsic instructions in AUTOSAR software modules.

## Slide 19: Thank you