## Slide 1: DGS Coding Guidelines Sharing Compiler Independency (MDG1, AUTOSAR)

## Slide 2: Agenda
DGS Coding Guidelines Sharing
RBVH/EJV3 | 2018-08-06
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
2
5.4.6 Compiler header files
5.4.7 Compiler internal defines
5.4.8 C−language implementation defined behavior
5.4.9 C99 extensions
5.4.10 Compiler extensions

## Slide 3: Compiler header files
DGS Coding Guidelines Sharing
RBVH/EJV3 | 2018-08-06
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
3
At DGS in general none of the compiler specific C−header and libs are allowed. The reason is that they might turn out to be a portability issue because:
  multiple implemented within a single compiler (example: limits.h),
  quite different about the content,
  using compiler internals,
  difficult to understand.
  From on MDG1 the header stddef.h is provided.
components which include stddef.h are not backwards compatible to older compiler releases, because in older compiler releases the headers were not included.
According to the MISRA recommendation the macro offsetof, in library <stddef.h>, shall not be used. This rule is also part of the agreed MISRA subset for DGS and therefore this macro shall not be used.

## Slide 4: Compiler internal defines
DGS Coding Guidelines Sharing
RBVH/EJV3 | 2018-08-06
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
4
The compilers internally (in the executable) set some defines, handling for example compiler issues (version, features), target issues (target/derivative type), CPU errata workarounds, limits, configuration (for example of FPU Floating Point unit). At DGS compiler defines shall not be used.
For example compiler defines shall not be used:
  writing code for different compilers within the same source file,
    #if defined tricore
    /* any TriCore specific code here */
    #elif defined WIN32
    /* any Windows specific code here */
    #else
    #error This code only works for TriCore and Win32
    #endif

## Slide 5: Compiler internal defines
DGS Coding Guidelines Sharing
RBVH/EJV3 | 2018-08-06
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
5
  hardware Configuration specific code
    #ifndef __HARD_FLOAT__
    #error This code requires a FPU (Floating Point Unit)
    #else
    /* any useful code here */
    #endif
    compiler extensions
      #if !defined(__tricore__)
      /* TriCore compiler uses _bit type. It is limited */
      /* to global and static variables */
      typedef unsigned char _bit;
      #endif

## Slide 6: C−language implementation defined behaviour
DGS Coding Guidelines Sharing
RBVH/EJV3 | 2018-08-06
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
6
The C−Standard is not fully specified, there is some freedom in implementation of the standard. Therefore some C constructs behave implementation−defined or even undefined. These constructs are critical for portability to another compiler. The risk of portability problems related to certain rules is given in appendix B Risk Factor.
  Do not make or use assumptions about the alignment of structure elements or variables.
  Do not make assumptions about endianness (little endian / big endian).
  Do not make or use assumptions about the size of structures. Determine the size of structures using the sizeof operator.
  Structures elements may not be accessed by pointers! There is a different high−/low−byte memory order for the different processor generations. This results in a wrong access if the readable or writable address is greater than 8 bit. This problem is directly visible in combination with unions.
  Do not make or use assumptions about the address of structure elements. Determine the address of structure elements using the & operator.

## Slide 7: C−language implementation defined behaviour
DGS Coding Guidelines Sharing
RBVH/EJV3 | 2018-08-06
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
7
  Unions are allowed only in the way ISO−C99 guarantees the implementation.
  Bit fields like defined in ISO C ( Example: struct {uint8 var : 5} ) are allowed only in the way ISO−C99 guarantees the implementation.
  Do not take any assumption about the size of an enumerated type.
  Use floating point programming only when absolutely necessary. In this case, separate floating point code (use macros or procedures if necessary). Limit floating point code to a few files. Avoid floating point interfaces: in this case components can be exchanged without dependencies to other components.

## Slide 8: C99 extensions
DGS Coding Guidelines Sharing
RBVH/EJV3 | 2018-08-06
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
8
For inline functions the keyword inline shall not be used in the C−code directly. Its use is restricted to central header files. This means, that inline functions shall only be defined by using the inline macro.
  Caution: The macro MEMLAY_USE_FORCE_INLINE is supported for MDG1, but is not allowed for AUTOSAR components. The macro INLINE_FUNCTION is supported for MDG1, but is not allowed for AUTOSAR components
  _Pragma is a C99 keyword. Its use is restricted to central header files.

## Slide 9: Compiler extensions
DGS Coding Guidelines Sharing
RBVH/EJV3 | 2018-08-06
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
9
Compiler extensions are generally not portable and shall not be used inside the C−code. If needed, central macros shall be provided which encapsulate the compiler keyword.
  _bit, the single bit type is TriCore/GNU specific and therefore not portable. Single bits shall only be specified by using the simple modelTYP_SingleBit.
  All use of __attribute___ ((<GNU extension>)) is not allowed, because these language extensions provided by the GNU compiler are not portable to other systems.
    Especially packing of a structure __attribute__ ((packed)) is not allowed.
    Especially __attribute__((always_inline)) is not allowed.
    The typeof operator is a compiler extension and is therefore not allowed.
    The TriCore/Gnu specific possibility to use brackets ({...}) ist not allowed.
    The keyword __inline__ is compiler specific and not allowed.

## Slide 10
RBVH/EJV3 | 2018-08-06
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
10
THANK YOU!