## Slide 1: DGS Coding Guidelines Variables and Messages

## Slide 2: Tables of Contents:
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
2
Overview
Process local variables
Bits and boolean variables/messages
Messages
Shared global data
FC local variables and file local variables
Global variables

## Slide 3: Overview
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
3
In general there’re two possibilities to specify variables in MEDC17 SW:
  Global and file local variables are specified using the MSR use case PaVaST.
  Process local variables are defined directly in the C−Code.
The following categories of variables are strictly distinguished:
  VALUE − variables of arithmetic type (integer type or float type)
  BIT − variable which keeps only two values (boolean)
  REFERENCE − variable which contains a memory access (pointer variable),
  STRUCTURE − named block of variables (structure with structure elements),
  TYPED_VALUE − variable with self defined data types.

## Slide 4: Overview
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
4
These variables types are used to differentiate the visibility in the interfaces between and inside function components:
  Global variables
  FC local variables
  File local variables
  Process local variables
To resolve data consistency conflicts in real time systems, variables shall be specified as Messages

## Slide 5: Overview
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
5
If variables are only needed for measurements in the calibration environment shall be specified as MEASUREMENT−POINT.
In the calibration environment :
  The variable has to be specified in the global data dictionary, a computation method.
  Data constraints (value range) can be specified to limit the range of the values stored in the variable (only ASCET−SD generated code).

## Slide 6: 6.5.1 Global variables
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
6
C−variables which have the storage class "extern" are called "global variables".
Global variables are specified as export variables in PaVaSt.
Other components can import these variables.
“Global to all the files contained in the complete PVER".
Global variables shall be additionally specified as messages.
SW−CALIBRATION_ACCESS shall be specified to be READ−ONLY.

## Slide 7: 6.5.2 Messages
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
7
MEDC17/MDG1 Message Definition:
The variable is accessed (read or written) from different processes.
The variable is defined on C−code level as "extern". This is the case if the variable is defined:
  with storage class "extern" in manual code
  in the global data dictionary in PaVaSt and owned and exported

## Slide 8: 6.5.2 Messages
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
8
The other way around:
  A variable is not a message in the MEDC17/MDG1 context if it is not used for interprocess communication or if it is defined as "static".
  Caution: static variables can have a consistency conflict if they are written/read from different processes inside the C−component!
Variables which are messages according to the given MEDC17/MDG1 message definition shall be specified as messages in PaVaSt.

## Slide 9: 6.5.2 Messages
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
9
In MDG1 the message concept MCOP (based on the MCOP tool, which is incorporated into the SW−Build tool chain) is used to ensure data consistency See Chapter 6.15 "DGS message concept " [MCOP] p. 110 .
How to specify the message access in PaVaSt is given in See Chapter 7.6.6.1.2 "Messages" p. 144 .
In case of messages there are detailed rules for the naming convention during roll−out of the message concept. The details are described in the DGS Naming Convention Guideline See Chapter 2 "Applicable Documents" p. 13.

## Slide 10: 6.5.3 Shared global data
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
10
Interfaces between SW components are global variables.
The interfaces for application SW are defined in PaVaSt files and from there are processed to A2L and header files
Software of the layers which are more close to hardware often use global data for better run−time behavior or more comfort when testing the software.
Notes: Interfaces between SW components in the MEDC17 application software are usually realized as global variables
In the MEDC17 application software, the interfaces for application SW are defined in PaVaSt files and from there are processed to A2L and header files
Other software of the layers which are more close to hardware often use global (extern) variables or (file−)global data for better run−time behavior or more comfort when testing the software.

## Slide 11: Known problems with global variables
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
11
Concurrency issues
Maintenance over the years and solving bugs is hard.
Tight coupling
Notes: Concurrency issues
In a real time system like MEDC17 processes of different priorities can interrupt. This can lead to writing and reading conflicts if a shared
data is accessed from different processes.
Maintenance over the years and solving bugs is hard.
Globals can be modified across files, multiple times at multiple places making it hard to detect root causes of bugs. Also the correction is
error prone because of the risk of side effects. For the similar reasons also the maintenance effort and review effort increases drastically.
Tight coupling
The SW components and layers are tightly coupled to each other. One cannot be changed independently of the other. Porting is affected.

## Slide 12: Rules for shared global data
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
12
Import/Export rule
The message concept shall be used to avoid conflicts
All shared global data which has to be assured.
Maintenance cost must to be consider
SW components should exchange information via APIs (function calls)
Notes: The sender/writer module owns and exports the interface, while the receiver/reader module imports it.
At DGS the message concept shall be used to avoid conflicts (read and write conflict, conflict in case of variable dependency)
All shared global data which are written or read from different priority levels data consistency has to be assured. This means that for all multiple read and write access to global data possible interrupts need to be considered and solved
Although using implicit mechanisms often improves code efficiency, this benefit must be weighed against the increased maintenance cost.
SW components should exchange information via APIs (function calls) to reduce the complexity of the code and to avoid concurrency problems

## Slide 13: 6.5.4 FC local variables & file local variables
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
13
FC local variables which shall be measured
File local variables used in different process priority levels
File local variables (statics)
static sint16 myStat = 1234; /* Initialized static variable */
Notes: FC local variables which shall be measured
- FC local variables are not exported to other components. They are only owned by the FC. In the C−code realization this means, that the
variable is only referenced in the header of this FC, but not in another header.
- During the SW−build a check assures that no other FC imports this variable, which is not exported.
- If this variable is required for measurements in the calibration tool then it is specified in the global data dictionary in PaVast See Chapter
7.6.2.4 "Local/Global data dictionary" p. 131
File local variables used in different process priority levels
If a file local variable is used in several processes with different priority levels then the variable is specified in PaVaSt as message to assure
data consistency.
File local variables (statics)
If a file local variable is used inside several processes with the same priority and if the variable is not needed for measurement in the
calibration tool then the variable shall be defined directly in the C−file. The storage class is then "static". In this case the variable has internal
linkage. Other functional components can not access this variable.
Without explicit #pragma shell the variable is located in the "default" section in memory.

## Slide 14: 6.5.5 Process local variables
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
14
Process local variables are defined at block scope
Notes: Process local variables
Process local variables are defined at block scope (process−level, (C−)function−level or method−level) in the C−file. These variables are not
specified via PaVaSt. They do not use storage and their value is undefined after the program has returned from the block. These variables
have to be assigned before usage.