## Slide 1: DGS Coding Guidelines Calibration parameters

## Slide 2: Tables of Contents:
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
2
Specification of calibration parameters
Bypass intervention points
Data initialisation for parameters, maps and curves
Sizing concept for axis points
Variant Coding
Access of calibration parameters in the C−Code

## Slide 3: 6.6.1 Specification of calibration parameters
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
3
  Calibration Parameter:
  is a data object which is adjusted, measured and displayed within a calibration tool and is not changed during runtime.
  are a special type of constants. Constant pointers to calibration values are not allowed due to the special addressing mode.
  Reason:
  Calibration values use *DSERAP addressing mode: they are accessed over a pointer table that changes during calibration. This saves code and allows calibration without any special hardware features.
  * BOSCH specific Online calibration method known as (D)SERAP: (Dynamic) SERial Application with Programming

## Slide 4: 6.6.1 Specification of calibration parameters
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
4
Example:
Definition in the data dictionary specification of the FCT PaVaSt file
<SW-DATA-DICTIONARY-SPEC>
…
<SW-CALPRMS>
…
</SW-CALPRMS>
…
</SW-DATA-DICTIONARY-SPEC>

## Slide 5: 6.6.2 Access of calibration parameters in the C−Code
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
5
Interpolation macros:
  Curves and maps shall not be accessed directly in the C−code but the macros which are provided by the DGS tool chain shall be used.
  This allows:
    the provision of several downscaling mechanism for curves and maps also at calibration time
    flexibility in defining the access to the parameters
    avoids errors in maintaining the code.

## Slide 6: 6.6.2 Access of calibration parameters in the C−Code
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
6
Dependent of the different PaVaSt types for DS classic, GS classic and DGS different interpolation / access−macros are provided.
The different types of PaVaSt files and their meaning is described in See Chapter 6.11 "Code syntaxes" The names are listed in the code syntax table which is given in See Chapter 2 "Applicable Documents“
Lesson learned Case:
The consistency between PaVaSt file and C−Code always has to be considered
In the LL case below, In the C−Code the interpolation macro was not used.
Caution: The developers (manual code) can not rely that the macro is used in the C−code. So always the usage has to be checked, when changing the definition in the PaVaSt file!)

## Slide 7: 6.6.2 Access of calibration parameters in the C−Code
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
7
Example:
PaVast:
<SW-MAX-AXIS-POINTS>4</SW-MAX-AXIS-POINTS> /* was changed from 3 to 4 */
C-Code:
ZFC_dBPFacNumAct[ct] = SrvX_IpoGroupMapS16 (intervalN, ct, 3 /*Number of axis points was not changed */, ZFC_dBPFacFBCG3_GM )
Correct DS:
ZFC_dBPFacNumAct[ct]= ZFC_dBPFacFBCG3_GMM(intervalN,ct);
Correct (DS TM1):
ZFC_dBPFacNumAct[ct] = ZFC_dBPFacFBCG3_GM_Get(intervalN,ct);

## Slide 8: 6.6.2 Access of calibration parameters in the C−Code
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
8
Instructions:
  Rule 1. The interpolation of a group axis may be used only at one place per PVER.
  Exception 1: The tasks with the interpolation of the same group axis run never parallel AND/OR never interrupt each other. (Example: 10ms−Task, Ini−Task, ReIni−Task).
  Exception 2: The interpolation of the group axis and the usage of the result as input for the interpolation of grouped curve(s) or/and map(s) are in the same process of the same FC. In this case the interpolation of the group axis can be called even more than once.
  Rule 2. Consider, the interpolations of several group axis could run on different tasks and/or cores. This means, that the inputs of a grouped map x and y could be taken from different timestamps depending on the scheduling.

## Slide 9: 6.6.2 Access of calibration parameters in the C−Code
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
9
Description:
Grouped curves are used when several curves use the same description x−axis (input axis), grouped maps are used when several maps use the same description x− and y− axis (input axes). Several curves/maps calculate their interpolation values from the same input value(s).
A grouped curve / map is a calibration object to specify functions with one input variable w=f(x) or w=f(x,y).
It shares the used x−axis with other curves or x− and y−axis with other maps (axis is defined as calibration parameter AXIS_VALUES)
The x−axis (and with maps additional the y−axis) is an one dimension array with the axis values.

## Slide 10: 6.6.2 Access of calibration parameters in the C−Code
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
10
Description:
The DPSearch (also called "DistrSearch", "Search" or at ASCET "distribution") evaluates with the value of the input variable x the index in the x−axis array and the ratio.
The Result of the DPSearch (index and ratio) of the x−axis is stored in a global variable/structure. (Maps store the index and ratio of the y−axis in a further global variable/structure). Attention: This global variable/structure does not have consistency protection (e.g. by MCOP).
The IPO services (also called "Interpolation","Get" or at ASCET "grouped Curve/Map") read this global variable/structure of this x−axis (with maps additional y−axis) and calculates the interpolation value.

## Slide 11: 6.6.3 Data initialisation for parameters, maps and curves
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
11
1. PaCoIn: data initialisation (called Neutral Calibration) within the FC. See See Chapter 7.6.14 "Initialisation values PaCoIn" [InitValues] p. 193 for an example. The rules for neutral calibration are given in the DGS−EC Process library by the following task descriptions:
  Create and maintain the relevant configuration files
  and in
  Provide the calibration for the package
2. default: no explicit data initialisation. Default setting is done by DAMOS.
3. from "Konserve" *.dcm File.

## Slide 12: 6.6.4 Sizing concept for axis points
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
12
In order to save ECU-resources or due to accuracy aspects the number of axis points needs to be reduced or increased after package integration
This means the number of axis points need to be changed after the C−Code is already tested and released
For MEDC17 two mechanism are provided:
    The number of axis points can be adjusted by using a "Konserve" *.dcm file or sizing artefact (standard case)
    The number of axis points can be made variant by using an adjustable system constant (special case)

## Slide 13: 6.6.4 Sizing concept for axis points
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
13
Due to the large number of curve/map axis points, there are some C-Coding rules for axis points:
  The number of axis point have to be coded as value within the maps or curves. In this case the number of axis points shall not be used hard coded within C−Code, because the number might change when the sizing artefact is applied.
  The number of axis points shall not be defined as adjustable system constants, except for the special case, that the number of axis points is used within the C−code. Adjustable system constants for the number of axis points shall be used sparsely, because the value have to be set by the integration.
  The number of axis points shall not be defined as calibration parameter, because it has to be set during calibration.

## Slide 14: 6.6.5 Variant Coding
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
14
Variant coding is used to handle different data in an ECU which are applicated for different kinds of engines and/ or vehicles.
Multiple data values of individual calibration parameters are stored in the ECU, the current variant of each element is selected by the variant criterion
Two different types of variant coding: pre/ during sw−build and post sw−build

## Slide 15: 6.6.5.1 Variant Coding in the different SW−Build tool chains
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
15
DS Variant Coding: DSERAP vectors used to switch over to a new value set.
GS Variant Coding: Variant coding method works on level of labels. When adding new variants of a parameter a new make is required.
DGS Variant Coding: Criteria and possible values are specified in VarCod.xml. The tool chain generates a header which contains the data initialization code. (DGS variant coding is under construction and not yet active.)

## Slide 16: 6.6.6 Bypass intervention points
RBEI/EEP1 | 9/23/2016
© Robert Bosch Engineering and Business Solutions Vietnam Company Limited 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
16
In general, new driving functions are developed graphically by tool (e.g. ASCET)
In some cases, the functions that already exist have to be replaced and in others cases, new functions have to be added
Preferably, these functions should not only be tested on the PC, they should also be tested in real time coupled with the ECU functions that already exist
The development methodology ”bypass” was developed for this purpose because bypass hooks are necessary in order to let the calculated data of new functions flow into the existing functions
This chapter is clarifying and has to be reworked for DGS