## Slide 1
Internal | Duong Cao Trong Nhan (RBVH/EJV24) | 07/24/2023
GATEWAY

## Slide 2
Internal | Duong Cao Trong Nhan (RBVH/EJV24) | 07/24/2023.
Overview
Tester
CGW
VCU
Gateway
Customer requirement: while flashing new software is happen between Tester and VCU, lower ECUs can still continue to work and communicate with the Tester via the VCU as a gateway.

## Slide 3
Internal | Duong Cao Trong Nhan (RBVH/EJV24) | 07/24/2023.
Solution
CAN→ CANIf → PDUR → another CANIf → CAN
CAN→ CANIf → CanTp → PduR→ DCM
Changing the concept mapping in each layers with gateway messages
Diagnostic messages: CAN→ CANIf → CanTp → PduR→ DCM
Gateway messages: CAN→ CANIf → PDUR → another CANIf → CAN

## Slide 4
Internal | Duong Cao Trong Nhan (RBVH/EJV24) | 07/24/2023.
Solution
HW Object
CAN Controller 1
Mailbox
CAN Transceiver 1
CAN Driver
HTH
HRH
HTH
HRH
PDU
PDU
CanIf
HW Object
CAN Controller 2
Mailbox
CAN Transceiver 2
Routing Table
PDUR
PduRDestdu
PduRSrcPdu
How the signal is handled through the layers for the gateway
Gateway messages: CAN→ CANIf → PDUR → another CANIf → CAN