## Slide 1: Reprogramming in DA RADAR
Internal | hop2hc (EVH/EMB3) | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Prepared by:
Reviewed and validated by:
Phan Thanh Hoang
Usha Manohar
Vignesh Prakash

## Slide 2: Agenda
Internal | hop2hc (EVH/EMB3) | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Reprogramming in DA RADAR
MRR1 & LRR4 Flash layout
Features of Boot loader
Programming sequence
Reprogramming by Diagnostic services

## Slide 3: MRR1 & LRR4 Flash layout
Internal | hop2hc (EVH/EMB3) | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Reprogramming in DA RADAR
There are multiple blocks in ECU flash for different purposes.
Memory layout is design not only to cover the flash, but also NVM implementation (EEPROM)
Number of blocks and ranges for each one could be configured statically in linker command file (.lcf)
Notes: In MRR1/LRR4, NVM is implemented as AUTOSAR compliant.
Actually, the PPC doesn’t have EEPROM, so NVM is mostly based on FEE (Flash EEPROM emulation), and abstracted by the MemIf layer.

## Slide 4: MRR1 & LRR4 Flash layout
Internal | hop2hc (EVH/EMB3) | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Reprogramming in DA RADAR
The first block is the root key, it contains the instruction to jump to BoschBootBlock
Next is the pointer table 1 – which points to factory parameters
Factory-data contains a lot of information about customer.
  This section of memory only be modified in plant.
  Application may read data from here for some particular purposes, e.g. ECU spare part number, component ID, hardware number...

## Slide 5: MRR1 & LRR4 Flash layout
Internal | hop2hc (EVH/EMB3) | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Reprogramming in DA RADAR
Next is Antenna Diagram section, it contains Antenna data only
Both pointer tables (1 and 2) have the same structure, but inverted.
  Pointer table 1 is for Factory data mapping, start address is fixed, end address is dynamic
  Pointer table 2 is for Antenna data mapping, start address is dynamic, end address is fixed

## Slide 6: MRR1 & LRR4 Flash layout
Internal | hop2hc (EVH/EMB3) | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Reprogramming in DA RADAR
Next is BoschBootBlock, which contains the instruction to be executed before entering customer specific bootblock (FBL)

## Slide 7: MRR1 & LRR4 Flash layout
Internal | hop2hc (EVH/EMB3) | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Reprogramming in DA RADAR
The CPB contains customer specific data, e.g. Checksum for HEX patch, software version check consistency, BOSCH constant parameter (class C and D)

## Slide 8: MRR1 & LRR4 Flash layout
Internal | hop2hc (EVH/EMB3) | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Reprogramming in DA RADAR
DriveBlock is the main section for application’s instructions. It maybe divided into several smaller sections for different purposes
There are 2 pages of NVM – which support for inter-software component communication
The NVM is implemented above memory interface, which mostly from Flash EEPROM emulation.

## Slide 9: Introduction
Internal | CC-DA/EST2 - RBEI/EAC1 | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Flash Bootloader
What is Flash Bootloader ??
It is a Program to program (Flash) the Application software and other operating data.
Why Bootloader ??
  When a ECU is first powered on, it may not have any Application Software in Flash or RAM.
  ECU must initially execute a small program stored in Flash along with the bare minimum of data needed to access all the devices from which the Application Software and data are loaded into Flash/RAM.
  To allow erasing and programming new applications on ECU in case of application updates, configuration changes.

## Slide 10: Features of Flash Bootloader
Internal | CC-DA/EST2 - RBEI/EAC1 | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Flash Bootloader
Resides in Flash memory and always the first application to run after reset.
Flash bootloaders are based on communication protocol such as CAN, Flexray etc.
Flash Bootloaders use a Diagnostic protocol to communicate and download to an ECU
An ECU has at least two partitions (Application and Bootloader)
Bootloader and application contains separate program code for Communication functions (COM stack)
Bootloader guarantees the programming of ECU even after the interruptions such as voltage, communication interruptions.

## Slide 11: Bootloader Architecture
Internal | CC-DA/EST2 - RBEI/EAC1 | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Flash Bootloader
Bootloader
Diagnostic Services
TP
Communication Driver (CAN/Flexray)
EEPROM Driver
EEPROM Data Handling
Microcontroller
Timing Module

## Slide 12: Diagnostic functionality in Flash Bootloader (Based on UDS)
Internal | CC-DA/EST2 - RBEI/EAC1 | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Flash Bootloader
DiagnosticSessionControl ($10)
ECU Reset ($11)
ReadDataByIdentifier ($22)
Security Access ($27)
Communication Control ($28)
WriteDataByIdentifier ($2E)
Routine Control ($31)
Request Download ($34)
Transfer Data ($36)
Request Transfer Exit ($37)
Tester Present ($3E)
ControlDTCSettings ($85)

## Slide 13
Internal | CC-DA/EST2 - RBEI/EAC1 | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Flash Bootloader
Session Transition

## Slide 14: Programming Sequence
Internal | CC-DA/EST2 - RBEI/EAC1 | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Flash Bootloader
Pre-programming
Programming Execution
Post-programming

## Slide 15: Pre-programming
Internal | CC-DA/EST2 - RBEI/EAC1 | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Flash Bootloader
After Startup, ECU will be in Default Session of Application or Bootloader
Preprograming sequence is carried out before
  Transferring to Bootloader (if in application default session) OR
  Initiating programming request (if in Bootloader default session)
SEQUENCE
Switch to Extended Diagnostic session
Check Programming Preconditions (Routine Control).
  Engine speed, Vehicle Speed, Temperature etc.
DTC setting off
  DTC logging is disabled
Block Inter-ECU communication

## Slide 16
Internal | CC-DA/EST2 - RBEI/EAC1 | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Flash Bootloader
NVM
CUSTOMER BOOT BLOCK
BOSCH BOOT BLOCK
FACTORY DATA
DRIVE BLOCK
Contains the Diagnostic services for flashing
JUMP TO PROGRAMMING
SESSION
Programming sequence
Flash Bootloader
Flash Bootloader
Flash Bootloader

## Slide 17
Internal | CC-DA/EST2 - RBEI/EAC1 | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
NVM
CUSTOMER BOOT BLOCK
BOSCH BOOT BLOCK
FACTORY DATA
DRIVE BLOCK
RAM AREA
FLASH TOOL
1) SEND DIAGNOSTIC REQUEST FOR DOWNLOADING FLASH ROUTINES TO RAM
Flash Bootloader
2) DOWNLOAD FLASH ROUTINES TO RAM AREA

## Slide 18
Internal | CC-DA/EST2 - RBEI/EAC1 | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Flash Bootloader
NVM
CUSTOMER BOOT BLOCK
BOSCH BOOT BLOCK
FACTORY DATA
DRIVE BLOCK
RAM AREA
FLASH TOOL
3) SEND DIAGNOSTIC REQUEST FOR DOWNLOADING DRIVE BLOCK TO RAM
4) CBB INVOKES THE RAM AREA AS PER THE REQUEST SENT
5) FLASH ROUTINES ARE UTILISED FOR ERASING AND FLASHING THE DRIVE BLOCK
Flash Bootloader
Flash Bootloader
Flash Bootloader
Flash Bootloader

## Slide 19: Programming Execution
Internal | CC-DA/EST2 - RBEI/EAC1 | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Flash Bootloader
Switch to Programming Session
Request for Security Access (Seed and Key algorithm)
Write Fingerprint (Tester serial Number, Programming Date)
Erase the required Memory
Request for the Download of software
Transfer the Software Data
Request for exiting from Data transfer
Check Programming Dependencies
Reset the ECU
Note: If the flash routines are not part of the Bootloader, these have to be loaded into RAM using the above sequence (Except ECU Reset) before flashing to Flash sections.

## Slide 20: Post-programming
Internal | CC-DA/EST2 - RBEI/EAC1 | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Flash Bootloader
Enable Inter- ECU communication
Enable DTC logging
Switch to Default Session

## Slide 21: Reprogramming by Diagnostic services
Internal | hop2hc (EVH/EMB3) | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Reprogramming in DA RADAR
Application and FBL usually share information through NVM interface.
Once the reprogramming request is accepted, the application shall set a flag to this interface, perform all necessary actions for pre-programming sequence then reset ECU to pass the control to FBL
Notes: The reprogramming function is the one to enable the software renewal of the electronically controlled controller(following ECU) in vehicle(through connector adapted for car diagnosis), or single state, using a particular communication function

## Slide 22: Reprogramming by Diagnostic services
Internal | hop2hc (EVH/EMB3) | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Reprogramming in DA RADAR
Reprogramming always has some common requirements: executes in programming session, passes security access.
The diagnostic system shall also take care of some other special precondition check, and follow the pre-programming sequence: disable DTC logging, block ECU communication
After all, it shall set the reprogramming flag into NVM then perform a software reset

## Slide 23: Reprogramming by Diagnostic services
Internal | hop2hc (EVH/EMB3) | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Reprogramming in DA RADAR
There are many diagnostic services involve into the reprogramming features
FBL interaction – set or reset the shared reprogramming flag in NVM – is always the key of reprogramming
It will be done by a particular service, that service is different from customer by customer.
  Suzuki: RequestDownload ($34)
  Nissan: StartDiagnosticSession ($10 $85)
  MMC:
  FIAT:
  HKMC:
  ...

## Slide 24: References
Internal | hop2hc (EVH/EMB3) | 30/05/2014 | © Robert Bosch Engineering and Business Solutions Limited 2014. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
Reprogramming in DA RADAR
FLASH_TOOL_Diatester.ppt – Vignesh Prakash
Adressbereiche_MRR1_LRR4_Release_5_higher.xls – Jochen Klier
JP customer requirements